## Slide 1: Department of electronics and communication engineering NIGHT PATROLLING ROBOT WITH SOUND DETECTION For SECURITY USING Iot STUDENT NAME 1 : MANDEPUDI DEEPAK KUMAR (37130237) STUDENT NAME 2 : BODAPOTHULA SAI RAM (37130063) PROJECT GUIDE : Mr. L. JEGAN ANTONY MARCILIN M.Tech., Assistant Professor Department of Electronics and communication engineering SatHyabama Institute of Science and Technology
SATHYABAMA INSTITUTE OF SCIENCE AND TECHNOLOGY
Chennai - 600119

## Slide 2: AbSTRACT
Safety is the biggest priority in the world. Surveillance and monitoring of our homes has seen a growing need in emerging times.
Development of night patrol that robot is used to find the sound waves in the surroundings, and security patrolling services.
It records and begins to relay photographs of the situation immediately after identification of the sound or human face. Then it sends the particular image to the given mail id and cloud.
The robot is able to perform security patrols during the night while functioning as a guide during the day.
The movement of a robot is also controlled automatically through obstacle detecting sensors to avoid the collision.
We designed and implemented a robust, easy to assemble, anthropomorphic security robot aiming to patrol large indoor areas, welcome, provide information and guide clients to their destination, as well as function as a telepresence platform for the human security guards.
Our project suggests that Robot is user friendly and pleasing to the people, it can perform security for human being.

## Slide 3: LITERATURE SURVEY 1:

## Slide 4: LITERATURE SURVEY 2:

## Slide 5: LITERATURE SURVEY 3:

## Slide 6: LITERATURE SURVEY 4:
S.NO | TITLE | AUTHOR | YEAR | DESCRIPTION
1 | Low-level pedestrian Detection by means of visible and Infra-red Tetravision | M.Bertozzi | 2015 | Far infra-red cameras are suitable for the detection of objects warmer (or colder) than the background (pedestrians, moving vehicles,…),since they are sufficiently contrasted with respect to the background.

## Slide 7: Objectives
Existing
In existing system, we can’t monitor the sound.
There is no facility of IOT.
In existing camera is not available.
To develop night patrol robot used to find the sound waves in the surroundings, and provide security patrolling services.
The idea behind this is to secure the whole area.
Raspberry Pi connected with the camera plays an important role in making an automatic robotic system.

## Slide 8
Proposed System
The proposed system can be used for protecting human.
Sound sensor detect the sound, then it will activate the camera to capture the image by using Raspberry Pi camera.
Then captured images are send to the respective email id through IOT.

## Slide 9
Block diagram
Block diagram of Night patrolling robot with sound sensor

## Slide 10
Hardware requirements
software requirements
• Raspberry Pi • Sound Sensor. • Motor. • Driver IC. • Pi Camera. • SD Card. • HDMI to VGA Converter. • Monitor. • Keypad. • Mouse
• Raspbian OS. • Python.

## Slide 11: Raspberry pi :
CPU: Quad-core 64-bit ARM Cortex A53 clocked at 1.2 GHz
GPU: 400MHz Video Core IV multimedia
Memory: 1GB LPDDR2-900 SDRAM (i.e. 900MHz)
USB ports: 4
Video outputs: HDMI, composite video (PAL and NTSC) via 3.5 mm jack
Network: 10/100Mbps Ethernet and 802.11n Wireless LAN
Peripherals: 17 GPIO plus specific functions, and HAT ID bus
Bluetooth: 4.1
Power source: 5 V via Micro USB or GPIO header
Size: 85.60mm × 56.5mm
Weight: 45g (1.6 oz)
Low cost & Low current
High reliability
Module IO pins have 35u hard gold plating

## Slide 12: DC MOTOR
A DC motor is any of a class of rotary electrical machines that converts direct current electrical energy into mechanical energy.
The most common types rely on the forces produced by magnetic fields.
Nearly all types of DC motors have some internal mechanism, either electromechanical or electronic, to periodically change the direction of current in part of the motor.
A DC motor's speed can be controlled over a wide range, using either a variable supply voltage or by changing the strength of current in its field windings.

## Slide 13: SOUND SENSOR
A sound sensor is defined as a module that detects sound waves through its intensity and converts it to electrical signals.
The Sound Sensor is a microphone that allows your GrovePi or GoPiGo robot car to listen to sound strength, so you can control it to take a picture or move around based on changes in noise!
Sound waves propagate through air molecules, Such sound waves cause the diaphragm in the microphone to vibrate, resulting in the capacitance change.
Capacitance change is then amplified and digitalized for processing of sound intensity.

## Slide 14: PI CAMERA
The Raspberry Pi Camera Module is a 5MP CMOS camera with a fixed focus lens that is capable of capturing still images as well as high definition video. Stills are captured at a resolution of 2592 x 1944, while video is supported at 1080p at 30 FPS, 720p at 60 FPS and 640x480 at 60 or 90 FPS.

## Slide 15: Demonstration

## Slide 16: Code Implementation
import smtplib
from email.mime.text import MIMEText
from email.mime.multipart import MIMEMultipart
from email.mime.base import MIMEBase
from email import encoders
ser=serial.Serial(port='/dev/ttyUSB0',baudrate=9600,parity=serial.PARITY_NONE,timeout=1)
motor1=32
motor2=36
motor3=38
motor4=40
import RPi.GPIO as GPIO
import time
import picamera
import serial
import os.path
import cv2
from subprocess import Popen, PIPE
from picamera import PiCamera
from time import sleep

## Slide 17
def callback(channel):
if GPIO.input(channel):
print ("Sound Detected!")
##ser.write(b'image taken')
GPIO.output(motor1,False)
GPIO.output(motor2,False)
GPIO.output(motor3,False)
GPIO.output(motor4,False)
ser.write(str("IMAGE TAKEN").encode())
print("robot stop")
time.sleep(0.5)
camera = PiCamera()
sleep(1)
camera.capture('/home/pi/Desktop/patrolling robot/example.jpg')
sleep(5)
camera.stop_preview()
camera.close()
time.sleep(0.1)
GPIO.setwarnings(False)
channel=11
GPIO.setmode(GPIO.BOARD)
GPIO.setup(channel, GPIO.IN)
GPIO.setup(motor1, GPIO.OUT)
GPIO.setup(motor2, GPIO.OUT)
GPIO.setup(motor3, GPIO.OUT)
GPIO.setup(motor4, GPIO.OUT)
print ("start")
GPIO.output(motor1,1)
GPIO.output(motor2,0)
GPIO.output(motor3,1)
GPIO.output(motor4,0)
##time.sleep(3)

## Slide 18
part = MIMEBase('application','octet-stream')
part.set_payload((attachment).read())
encoders.encode_base64(part)
part.add_header('Content-Disposition',"attachment; filename= "+filename)
msg.attach(part)
text = msg.as_string()
server = smtplib.SMTP('smtp.gmail.com',587)
server.starttls()
server.login(email_user,email_password)
server.sendmail(email_user,email_send,text)
server.quit()
print("mail sent")
print ("mail")
email_user = 'sairambo****@gmail.com'
email_send = 'kumar****@gmail.com'
subject = 'RaspberryPi Took images'
email_password = 'Bo******'
msg = MIMEMultipart()
msg['From'] = email_user
msg['To'] = email_send
msg['Subject'] = 'python'
body = 'night patrolling robot!'
msg.attach(MIMEText(body,'plain'))
filename='/home/pi/Desktop/patrolling robot/example.jpg'
attachment=open(filename,'rb')

## Slide 19
GPIO.output(motor1,True)
GPIO.output(motor2,False)
GPIO.output(motor3,True)
GPIO.output(motor4,False)
else:
print("hi")
GPIO.add_event_detect(channel, GPIO.BOTH, bouncetime=300)
# let us know when the pin goes HIGH or LOW
GPIO.add_event_callback(channel, callback)
# assign function to GPIO PIN, Run function on change
while True:
time.sleep(1)

## Slide 20: Code execution

## Slide 23
PROJECT DEMO VIDEO

## Slide 24: OUTPUT

## Slide 25
FINAL RESULT
IMAGES RECEIVED TO MAIL

## Slide 27: ALERT MESSAGE NOTIFICATIONS FROM CLOUD THROUGH IOT

## Slide 28
References
Sushant Kumar and Dr. S. S. Solanki, “Remote Home Surveillance System “, 2016 International Conference on Advances in Computing, Communication, & Automation (ICACCA), 29 September 2016
JTutun Juhana and Vivi Gusti Anggraini, “Design and Implementation of Smart Home Surveillance System”, 2016 10th International Conference on Telecommunication Systems Services and Applications (TSSA), 6 March 2017
J. Zhang, G. Song, G. Qiao, T. Meng and H. Sun, "An indoor security system with a jumping robot as the surveillance terminal," in IEEE Transactions on Consumer Electronics, vol. 57, no. 4, pp. 1774-1781, November 2011.
G. Song, Z. Wei, W. Zhang and A. Song, "A Hybrid Sensor Network System for Home Monitoring Applications," in IEEE Transactions on Consumer Electronics, vol. 53, no. 4, pp. 1434-1439, Nov. 2007.
W. Lao, J. Han and P. H. n. De With, "Automatic video-based human motion analyzer for consumer surveillance system," in IEEE Transactions on Consumer Electronics, vol. 55, no. 2, pp. 591-598, May 2009.
C. Micheloni, G. L. Foresti, C. Piciarelli and L. Cinque, "An Autonomous Vehicle for Video Surveillance of Indoor Environments," in IEEE Transactions on Vehicular Technology, vol. 56, no. 2, pp. 487-498.
J.M. A´ lvarez and A.M. Lopez, “Road detection based on illuminant invariance”,Intelligent Transportation Systems, IEEE Transactions on, no. 99, pp. 1–10, 2010.

## Slide 29
Thank You!